## Slide 1: Cooperative Diversity
Caleb Zulawski
Spencer Chan

## Slide 2: Cooperative Schemes
Autonomous self-organizing networks:
  Wireless ad-hoc networks
  Wireless sensor networks
Requires nodes to relay data for other nodes when available
Reasons for implementation:
  Transmit longer distances with less power
  Transmit with diversity gain to combat multipath/shadow fading

## Slide 3: Direct Scheme
Data is transmitted from the source node to the destination node.
Destination responds with an ACK if the checksum matches the packet, or with a NACK otherwise.
S
3
1
2
D
Packet + CRC
ACK

## Slide 4: Relay Scheme (Cooperative)
The source sends data to an intermediate node, which relays the data to the destination.
S
3
1
2
D
Packet + CRC
ACK
Packet + CRC
ACK
ACK

## Slide 5: Cooperative Diversity Scheme
If the direct scheme fails, the packets are sent to nodes, which are used as multiple antennas to produce diversity gain.
Potential relays are chosen by those which receive a correct CRC and packet.
S
3
1
2
D
Packet + CRC
NACK
Packet + CRC
NACK
Packet + CRC
NACK
Packet + CRC
ACK
ACK
Packet + CRC
Diversity = 2

## Slide 6: Adaptive Cooperative Diversity
An adaptive scheme can choose which scheme to use depending on channel state.
Goal is to maximize quality of service

## Slide 9: Sources
L. Dai and K. B. Letaief. “Throughput Maximization of Ad-hoc Wireless Networks Using Adaptive Cooperative Diversity and Truncated ARQ.”
S. S. Ikki and M. H. Ahmed. “Performance Analysis of Cooperative Diversity with Incremental-Best-Relay Technique over Rayleigh Fading Channels.”